## Slide 1
Production and Operations Mgt
.
Monday 09 March 2020

## Slide 2: SUPPLY CHAIN MGT
Introduction
Supply chain management basically merges the supply and demand management. It uses different strategies and approaches to view the entire chain and work efficiently at each and every step involved in the chain.

## Slide 3: SUPPLY CHAIN MGT
Every unit that participates in the process must aim to minimize the costs and help the companies to improve their long term performance, while also creating value for its stakeholders and customers. This process can also minimize the rates by eradicating the unnecessary expenses, movements and handling.

## Slide 4: SUPPLY CHAIN MGT
Meaning
Supply Chain Management can be defined as the management of flow of products and services, which begins from the origin of products and ends at the product’s consumption. It also comprises movement and storage of raw materials that are involved in work in progress, inventory and fully furnished goods.

## Slide 5: SUPPLY CHAIN MGT
Objective
The main objective of supply chain management is to monitor and relate production, distribution, and shipment of products and services. This can be done by companies with a very good and tight hold over internal inventories, production, distribution, internal productions and sales.

## Slide 6: SUPPLY CHAIN MGT
Advantages
In this era of globalization where companies compete to provide the best quality products to the customers and satisfy all their demands, supply chain management plays a very important role. All the companies are highly dependent on effective supply chain process.

## Slide 7: SUPPLY CHAIN MGT
Advantages
Develops better customer relationship and service.
Creates better delivery mechanisms for products and services in demand with minimum delay.
Manage productivity and business functions.
Minimizes warehouse and transportation costs.
Minimizes direct and indirect costs.

## Slide 8: SUPPLY CHAIN MGT
Advantages
Assists in achieving shipping of right products to the right place at the right time.
Enhances inventory management, supporting the successful execution of just-in-time stock models.
Assists companies in adapting to the challenges of globalization, economic disturbance, expanding consumer expectations, and related differences.
Assists companies in minimizing waste, driving out costs, and achieving efficiencies throughout the supply chain process.

## Slide 9: SUPPLY CHAIN MGT
Supply Chain Decisions
There are four major decision areas in supply chain management: 1) location, 2) production, 3) inventory, and 4) transportation (distribution), and there are both strategic and operational elements in each of these decision areas.

## Slide 10: SUPPLY CHAIN MGT
1.Location Decisions
The geographic placement of production facilities, stocking points, and sourcing points is the natural first step in creating a supply chain. The location of facilities involves a commitment of resources to a long-term plan. Once the size, number, and location of these are determined, so are the possible paths by which the product flows through to the final customer.

## Slide 11: SUPPLY CHAIN MGT (Location)
These decisions are of great significance to a firm since they represent the basic strategy for accessing customer markets, and will have a considerable impact on revenue, cost, and level of service. These decisions should be determined by an optimization routine that considers production costs, taxes, duties and duty drawback, tariffs, local content, distribution costs, production limitations, etc

## Slide 12: SUPPLY CHAIN MGT
2. Production decisions
The strategic decisions include what products to produce, and which plants to produce them in. As before, these decisions have a big impact on the revenues, costs and customer service levels of the firm. These decisions assume the existence of the facilities, but determine the exact path(s) through which a product flows to and from these facilities.

## Slide 13: SUPPLY CHAIN MGT (Production)
Operational decisions focus on detailed production scheduling. These decisions include the construction of the master production schedules, scheduling production on machines, and equipment maintenance. Other considerations include workload balancing, and quality control measures at a production facility.

## Slide 14: SUPPLY CHAIN MGT
3. Inventory Decisions
These refer to means by which inventories are managed. Inventories exist at every stage of the supply chain as either raw materials, semi-finished or finished goods. They can also be in-process between locations. Their primary purpose to buffer against any uncertainty that might exist in the supply chain. Since holding of inventories can cost anywhere between 20 to 40 percent of their value, their efficient management is critical in supply chain operations.

## Slide 15: SUPPLY CHAIN MGT
4. Transportation Decisions
The mode choice aspect of these decisions are the more strategic ones. These are closely linked to the inventory decisions, since the best choice of mode is often found by trading-off the cost of using the particular mode of transport with the indirect cost of inventory associated with that mode. While air shipments may be fast, reliable, and warrant lesser safety stocks, they are expensive. Meanwhile shipping by sea or rail may be much cheaper, but they necessitate holding relatively large amounts of inventory to buffer against the inherent uncertainty associated with them.

## Slide 16: SUPPLY CHAIN MGT
Four Stages For An Effective Supply Chain
Stage 1: Supply Management. The most basic stage, built around an internal MRP system that is lead-time driven. It includes tier-one suppliers only. Most planned vendor interaction is through documentation and seldom involves status reporting. Communications are transactional and include quoting, purchase orders, and releases.

## Slide 17: SUPPLY CHAIN MGT
Stage 2: Supply Chain Management. This stage is characterized by an increased scope and includes tier-two suppliers and beyond. There is also increased interest in status reporting, some data sharing among participants, and generally more complex interrelationships. Communications are transactional with the addition of data flow.

## Slide 18: SUPPLY CHAIN MGT
Stage 3: Supply Chain Integration. Includes programs that benefit all members of the chain. It elevates supply to collaborative involvement among the members, including strategic planning and risk sharing. Communications at this level go well beyond transactions and data and include information of all types.

## Slide 19: SUPPLY CHAIN MGT
Stage 4: Demand-Supply Network Collaboration. Cooperative interaction and proactive behavior based on critical information that flows freely and simultaneously throughout the supply network. It is sometimes referred to as the glass pipe. I know of no examples of this stage in the electronics industry.

## Slide 20: INVENTORY MANAGEMENT
Introduction
Inventory mgt is an important aspect of any successful business. It is the process of overseeing and controlling the flow of inventory units a business uses in the production or manufacture of goods for sale or distribution. Inventories are usually made up of a combination of goods, raw materials and finished products, and effective management of these items is essential to ensure optimal stock levels and to maximize the earning potential of the company. It also allows a business to prevent or mitigate any inventory-associated losses.

## Slide 21: INVENTORY MANAGEMENT
Definition
Inventory is an idle stock of physical goods that contain economic value, and are held in various forms by an organization in its custody awaiting packing, processing, transformation, use or sale in a future point of time. Any organization which is into production, trading, sale and service of a product will necessarily hold stock of various physical resources to aid in future consumption and sale.

## Slide 22: INVENTORY MANAGEMENT
Inventory management types
1. Raw materials are any items used to manufacture components or finished products. These can be items produced directly by your business or purchased from a supplier.

## Slide 23: INVENTORY MANAGEMENT
2. Works-in-progress inventory refers to unfinished items moving through production but not yet ready for sale.

## Slide 24: INVENTORY MANAGEMENT
3. Finished goods are products that have completed the production process and are ready to be sold/ used.

## Slide 25: INVENTORY MANAGEMENT
4. Maintenance, repair, and operations (MRO) goods are items used to support and facilitate the production of finished goods. These items are usually consumed as a result of the production process but aren’t a direct part of the finished product.

## Slide 26: INVENTORY MANAGEMENT
Inventory Costs
Ordering Cost
Carrying Cost
Shortage or stock out Cost & Cost of Replenishment

## Slide 27: INVENTORY MANAGEMENT
1. Ordering Cost
Cost of procurement and inbound logistics costs form a part of Ordering Cost. Ordering Cost is dependant and varies based on two factors - The cost of ordering excess and the Cost of ordering too less. Both these factors move in opposite directions to each other. Ordering excess quantity will result in carrying cost of inventory. Where as ordering less will result in increase of replenishment cost and ordering costs.

## Slide 28: INVENTORY MANAGEMENT
2. Carrying Cost
Inventory storage and maintenance involves various types of costs namely: Inventory Storage Cost and Cost of Capital. Inventory carrying involves inventory storage and management either using in house facilities or external warehouses owned and managed by third party vendors.

## Slide 29: INVENTORY MANAGEMENT
Inventory Storage Cost
Inventory storage costs typically include Cost of Building Rental and facility maintenance and related costs. Cost of Material Handling Equipments, IT Hardware and applications, including cost of purchase, depreciation or rental or lease as the case may be. Further costs include operational costs, consumables, communication costs and utilities, besides the cost of human resources employed in operations as well as management.

## Slide 30: INVENTORY MANAGEMENT
Cost of Capital
Includes the costs of investments, interest on working capital, taxes on inventory paid, insurance costs and other costs associate with legal liabilities.The inventory storage costs as well as cost of capital is dependant upon and varies with the decision of the management to manage inventory in house or through outsourced vendors and third party service providers.

## Slide 31: INVENTORY MANAGEMENT
Concept And Meaning Of Stock Level
Stock level refers to the different levels of stock which are required for an efficient and effective control of materials and to avoid over and under-stocking of materials. The purpose of materials control is to maintain the sock of raw materials as low as possible and at the same time they may be available as and when required

## Slide 32: INVENTORY MANAGEMENT
Stock level includes:
Minimum stock level
Re-order stock
Maximum stock level
Average stock level
Danger stock level
EOQ/ Optimal inventory
JIT

## Slide 33: INVENTORY MANAGEMENT
Maximum Stock Level
Maximum level is that level of stock, which is not normally allowed to be exceeded. Beyond the maximum stock level, a blockage of capital should be exercised to check unnecessary stock. The factory should not keep materials more than the maximum stock level. It increases the carrying cost of holding unnecessary inventory level. It is the opportunity cost of holding inventory.

## Slide 34: INVENTORY MANAGEMENT
The maximum stock level can be calculated by using the following formula: Maximum Level = Re-order Level + Re-order quantity - (Minimum consumption X Minimum Delivery Time)

## Slide 35: INVENTORY MANAGEMENT
2. Re-order Level
Re-order level is a level of material at which the storekeeper should initiate the purchase requisition for fresh supplies. When the stock-in-hand comes down to the re-ordering level, it is an indication that an action should be taken for replenishment or purchase.

## Slide 36: INVENTORY MANAGEMENT
The re-order level is calculated as follows: Re-order Level= Minimum Level(Safety stock) + (Average lead time x Average consumption)
OR Re-order Level= Maximum Consumption x Maximum Re-ordering Period

## Slide 37: INVENTORY MANAGEMENT
Illustration Suppose, Maximum consumption per day = 400 units Minimum consumption per day = 200 units Re-order period = 8 to 10 days Then, Re-order Level = Maximum consumption x Maximum re-order period = 400 units x 10 days = 4000 units

## Slide 38: INVENTORY MANAGEMENT
Illustration
Re-order quantity = 1000 units Re-order Level = 1500 units Re-ordering period = 4 to 6 days Daily consumption = 150 to 250 units Maximum Level = ? Solution, Maximum Level = Re-order level + Re-order quantity - (Minimum consumption x Minimum Re-ordering period) = 1500+1000(150 x 4) = 1900 units.

## Slide 39: INVENTORY MANAGEMENT
3. The minimum level of stock
The minimum level of stock is a certain predetermined minimum quantity of raw materials or merchandise inventory which should always be available in stock in the normal course of business. The minimum level of inventory is a kind of a precautionary level of inventory which indicates that the delivery of raw materials or merchandise may take more than the normal lead time.

## Slide 40: INVENTORY MANAGEMENT
Lead time is the expected time taken by the supplier to deliver goods at the warehouse or at the point of consumption. If the level of stock strikes the minimum level, the management of the company must make sure that they corroborate with the supplier and take other necessary measures to make the goods (inventory or raw materials) available in time so that the business operations are not disturbed or delayed.

## Slide 41: INVENTORY MANAGEMENT
Formula:
The formulas used to calculate the minimum level of stock are given below:
Minimum Level of Inventory = (Maximum usage × Maximum lead time) – (Average usage × Average lead time) OR
Minimum Level of inventory = Re-order level – (Average usage × Average lead time)
NOTE: Both the formulas are equivalent and produce the same result.

## Slide 42: INVENTORY MANAGEMENT
Example 1
The Shop UNA sells T-shirts. Each shirt costs $15 and is sold for $20 to customers. The maximum demand is 20,000 shirts per year and the average demand is 18,570 shirts per year. The average lead time is 57 days and the maximum lead time is 64 days.
Required: Compute the reorder level and the minimum level of stock of T-shirts for Shop UNA

## Slide 43: INVENTORY MANAGEMENT
Solution
Maximum demand per day: 20,000 shirts/365 days = 55 shirts
Average demand per day: 18,570 shirts/365 days = 51 shirts
Reorder level = (Maximum demand × Maximum lead time) = (55 units × 64 days) = 3,520 units

## Slide 44: INVENTORY MANAGEMENT
Minimum level of stock = Reorder level – (Average demand × average lead time) = 3,520 units – (51 units × 57 days) = 3,520 units – 2,907 units = 613 units

## Slide 45: INVENTORY MANAGEMENT
Example 2
The MAT co. deals in cars. The selected data is given below:
Annual demand:
Maximum demand: 730 cars per year
Normal or average demand: 365 cars per year
Minimum demand: 283 cars per year
Lead time in days:
Maximum lead time: 98 days
Normal or average lead time: 87 days
Minimum lead time: 73 days
Required: Compute minimum level of inventory for MAT co. on the basis of above data.

## Slide 46: INVENTORY MANAGEMENT
Solution:
Maximum demand per day: 730 cars/365 days = 2 cars per day
Average demand per day: 365 cars/365 days = 1 car per day
Minimum level of inventory = (Maximum demand per day × Maximum lead time) – (Average demand per day × Average lead time) = (2 units × 98 days) – (1 unit × 87 days) = 196 units – 87 units = 109 units

## Slide 47: INVENTORY MANAGEMENT
Example 3
A company makes iron tables. To manufacture one table, 2.35 kgs of iron (raw material) is used. The details are given below:
Maximum demand for tables: 600 tables per month
Average demand for tables: 475 tables per month
Minimum demand for tables: 320 tables per month
Maximum lead time: 2.5 weeks
Average lead time: 1.9 weeks
Minimum lead time: 1.5 weeks
Required: Compute the minimum kilograms of iron that the company needs to maintain.

## Slide 48: INVENTORY MANAGEMENT
  Solution
Maximum Usage: 600 tables × 2.35 kgs = 1,410 kgs
Average Usage: 475 tables × 2.35 kgs = 1,116.25 kgs
Minimum level = (Maximum usage × Maximum lead time) – (Average usage × Average lead time)
= (1,410 kgs × 2.5 days) – (1,116.25 kgs × 1.9 days) = 3,525 kgs – 2,121 kgs = 1,404 kgs

## Slide 49: INVENTORY MANAGEMENT
4. Average Stock Level
Average Stock level shows the average stock held by a firm. The average stock level can be calculated with the help of following formula. Average Stock Level = Minimum Level + (1/2Re-order Quantity) OR Average Stock Level = (Minimum Level + Maximum Level)/2

## Slide 50: INVENTORY MANAGEMENT
Illustration
Re-order quantity = 2000 units Minimum Level = 500 units Average stock level = ? Solution, Average stock level = Minimum level + 1/2 x Re-order quantity = 500 + 1/2 x 2000 = 500+ 1000 = 1500 units.

## Slide 51: INVENTORY MANAGEMENT
5. Danger Level
Danger level is a level of fixed usually below the minimum level. When the stock reaches danger level, an urgent action for purchase is initiated. When stock reaches the minimum level, the storekeeper must make special arrangements to get fresh materials, so that the production may not be interrupted due to the shortage of materials.

## Slide 52: INVENTORY MANAGEMENT
The formula Danger Level = Normal consumption x Maximum re-order period for emergency purchase Illustration, Daily Consumption = 100 to 200 units Max. re-order period for emergency purchase = 5 days Danger Level = ? Solution, Danger Level = Normal consumption x Maximum re-order period for emergency purchase
= 150 x 5=750 units.

## Slide 53: ORDERING and HOLDING COSTS
6. Economic order quantity (EOQ)
It is the order size that minimizes the sum of ordering and holding costs related to raw materials or merchandise inventories. In other words, it is the optimal inventory size that should be ordered with the supplier to minimize the total annual inventory cost of the business. Other names used for economic order quantity are optimal order size and optimal order quantity.

## Slide 54: ORDERING and HOLDING COSTS
Ordering costs
The ordering costs are the costs that are incurred every time an order for inventory is placed with the supplier. Examples of these costs include telephone charges, delivery charges, invoice verification expenses and payment processing expenses etc. The total ordering cost usually varies according to the frequency of placing orders.

## Slide 55: ORDERING and HOLDING COSTS
Holding costs
The holding costs (also known as carrying costs) are the costs that are incurred to hold the inventory in a store or warehouse. Examples of costs associated with holding of inventory include occupancy of storage space, rent, shrinkage, deterioration, obsolescence, insurance and property tax etc. The total holding cost usually depends upon the size of the order placed for inventory.

## Slide 56: ORDERING and HOLDING COSTS
Assumptions/Limitations of EOQ
The total number of units to be consumed during the period is known with certainty.
The total ordering cost remains constant throughout the period.
The inventory cost remains constant throughout the period.
There are no cash or quantity discounts available.
The whole quantity of ordered inventory is delivered in one batch.
The optimal quantity for each invariable or stock item is computed separately.
The lead time does not fluctuate and the order is received on time with the total order quantity.

## Slide 57: ORDERING and HOLDING COSTS
Relation between the ordering and holding cost
There is an inverse relationship between ordering cost and holding cost. Keeping the annual demand constant if for example the number of orders decreases, the ordering cost will also decrease but the holding cost will rise and vice versa.

## Slide 58: EOQ
Economic order Qty Graph

## Slide 59: ORDERING and HOLDING COSTS
Formulae of EOQ
Where,
D = Demand per year
Co = Cost per order
Ch = Cost of holding per unit of inventory

## Slide 60: ORDERING and HOLDING COSTS
The material DX is used uniformly throughout the year. The data about annual requirement, ordering cost and holding cost of this material is given below:
Annual requirement: 2,400 units
Ordering cost: $10 per order
Holding cost: $0.30 per unit
Required: Determine the economic order quantity (EOQ) of material DX using above data.

## Slide 61: ORDERING and HOLDING COSTS
Solution

## Slide 62: ORDERING and HOLDING COSTS
The economic order quantity for material DX is 400 units. Now, we can compute the number of orders to be placed per year, annual ordering cost, annual holding cost and combined annual ordering and holding cost as follows:
Number of orders per year
= Annual demand/EOQ = 2,400 units/400 units = 6 orders per year

## Slide 63: ORDERING and HOLDING COSTS
Ordering cost
= Number or orders per year × Cost per order = 6 orders × $10 = $60
Holding cost
= Average units × Holding cost per unit
= (400/2) × 0.3 = $60

## Slide 64: ORDERING and HOLDING COSTS
Combined ordering and holding cost at economic order quantity (EOQ):
= Ordering cost + Holding cost = $60 + $60 = $120
Notice that both ordering cost and holding cost are $60 at economic order quantity. The holding cost and ordering cost at EOQ tend to be the same.

## Slide 65: EOQ
Average units × Holding cost per unit: 1,200 units × 0.30 = $360
Notice that the quantity of 400 units with 6 annual orders and a combined ordering and holding cost of $120 is the most economical quantity to order. Other order quantities that result in more or less than six orders per year are not so economical. For example, if only one order for the whole annual requirement of 2,400 units is placed, the combined ordering and holding cost comes to $370 which is far higher than the cost at economic order quantity of 400 units.

## Slide 66: ORDERING and HOLDING COSTS
Eg.2
The John Sports Inc. purchases tennis balls at $20 per dozen from its suppliers. The John Sports will sell 34,300 dozens of tennis balls evenly throughout the year. The total cost to handle a purchase order is $10. The insurance, property tax and rent for each dozen tennis balls in the average inventory is $0.40. The company wants a 5% return on average inventory investment.
Required:
a) Compute the economic order quantity.
b) Compute the total annual inventory expenses to sell 34,300 dozens of tennis balls if orders are placed according to economic order quantity computed in part 1.

## Slide 67: ORDERING and HOLDING COSTS
Solution

## Slide 68: ORDERING and HOLDING COSTS
*$0.40 + ($20 × 5/100) = $1.4
2. Total annual inventory expenses to sell 34,300 dozens of tennis balls:
= Annual ordering cost + Annual holding cost = (Number of orders × Cost per order) + (Average units × Holding cost per unit) = (*49 orders × $10) + [(700/2) × 1.4] = $490 + $490 = $980
*Number of orders to be placed: 34,300/700 = 49 orders

## Slide 69: INVENTORY MANAGEMENT
7. JIT
Just in time (JIT) inventory is a strategy to increase efficiency and decrease waste by receiving goods only as they are needed in the production process, thereby reducing inventory costs. In other words, JIT inventory refers to an inventory management system with objectives of having inventory readily available to meet demand, but not to a point of excess where you must stockpile extra products.

## Slide 70: JIT (Advantages)
Companies like to use JIT as it is seen as a more cost efficient method of holding stock. Its purpose is to minimize the amount of goods you hold at any one time, and this has numerous advantages:
Less space needed
Waste reduction
Smaller investments, etc

## Slide 71: JIT (Disadvantages)
JIT unfortunately comes with a number of potential disadvantages, which can have a significant impact on the company if they occur.
Risk of running out of stock
Lack of control over time frame
More planning required etc.

## Slide 72: PLANT LAYOUT & LOCATION
Meaning: Plant layout refers to the physical arrangement of facilities. It is the configuration of departments, work centres and equipment in the conversion process. The overall objective of the plant layout is to design a physical arrangement that meets the required output quality and quantity most economically.

## Slide 73: Types of Layout
1. Process Layout: Similar pieces of equipment that perform similar functions are grouped together. For example; all drill machines are grouped and placed together.
2. Product Layout: The pieces of equipment required to make a Particular product are grouped together, as in an Automobile assembly line.
3. Fixed Layout: The equipment is brought to the object being processed, and the object does not move. Example; house construction.

## Slide 74: TOTAL QUALITY MANAGEMENT (TQM)
Introduction
Total Quality Management is a management approach that originated in the 1950's and has steadily become more popular since the early 1980's. Total Quality is a description of the culture, attitude and organization of a company that strives to provide customers with products and services that satisfy their needs. The culture requires quality in all aspects of the company's operations, with processes being done right the first time and defects and waste eradicated from operations.

## Slide 75: TOTAL QUALITY MANAGEMENT (TQM)
Meaning
TQM is a management philosophy that seeks to integrate all organizational functions (marketing, finance, design, engineering, and production, customer service, etc.) to focus on meeting customer needs and organizational objectives.

## Slide 76: TQM ACTIVITIES
TQM is the foundation for activities, which include:
Commitment by senior management and all employees
Meeting customer requirements
Reducing development cycle times
Just In Time/Demand Flow Manufacturing
Improvement teams
Reducing product and service costs

## Slide 77: TQM ACTIVITIES
Systems to facilitate improvement
Line Management ownership
Employee involvement and empowerment
Recognition and celebration
Challenging quantified goals and benchmarking
Focus on processes / improvement plans
Specific incorporation in strategic planning
This shows that TQM must be practiced in all activities, by all personnel, in Manufacturing, Marketing, Engineering, R&D, Sales, Purchasing, HR, etc.

## Slide 78: Principles of TQM
The key principles of TQM are as following:
1. Management Commitment
  Plan (drive, direct)
  Do (deploy, support, participate)
  Check (review)
  Act (recognize, communicate, revise)
2. Employee Empowerment
  Training
  Suggestion scheme
  Measurement and recognition
  Excellence teams

## Slide 79: Principles of TQM
3. Customer Focus
  Supplier partnership
  Service relationship with internal customers
  Never compromise quality
  Customer driven standards
4. Continuous Improvement
  Systematic measurement and focus on CONQ
  Excellence teams
  Cross-functional process management
  Attain, maintain, improve standards

## Slide 80: TOTAL QUALITY MANAGEMENT
Quality Control (QC) may be defined as ‘a system that is used to maintain a desired level of quality in a product or service’. It is a systematic control of various factors that affect the quality of the product. Quality control aims at prevention of defects at the source, relies on effective feed back system and corrective action procedure.

## Slide 81: Quality control
Quality control can also be defined as ‘that industrial management technique by means of which product of uniform acceptable quality is manufactured’. It is the entire collection of activities which ensures that the operation will produce the optimum quality products at minimum cost.

## Slide 82: Objectives of quality control
The main objectives of quality control are:
To improve the companies income by making the production more acceptable to the customers i.e., by providing long life, greater usefulness, maintainability, etc.
To reduce companies cost through reduction of losses due to defects.
To achieve interchangeability of manufacture in large scale production.

## Slide 83
To produce optimal quality at reduced price.
To ensure satisfaction of customers with productions or services or high quality level,
To build customer goodwill, confidence and reputation of manufacturer.
To make inspection prompt to ensure quality control.
To check the variation during manufacturing.

## Slide 84: TOOLS TO MEASURE QUALITY
The ISO 9000 certification standards, created by the International Organization for Standardization, now play a major role in setting quality standards for global manufacturers. Many European companies require that their vendors meet these standards a condition for obtaining contracts.

## Slide 85: TOTAL QUALITY MGT_Conclusion
The principles of Total Quality Management are to seek to satisfy the external customer with quality goods and services, as well as your company internal customers; to satisfy your external and internal suppliers; and to continuously improve processes by working smarter and using special quality methods.

## Slide 86: SIX SIGMA
Meaning of Six Sigma refers to a set of management techniques intended to improve business processes by greatly reducing the probability that an error or defect will occur, it may have a generic or customized name for the organization like “Operational Excellence,” “Zero Defects,” or “Customer Perfection.” It was developed by Motorola in early to middle 1980’s based on quality management fundamentals.

## Slide 87: Six Sigma: DMAIC
Define (D)
  Identify customers and their priorities
  Identify a project suitable for Six-Sigma efforts based on business objectives as well as customer needs and feedback.
  Identify CTQs(critical-to-characteristics) that the customer considers to have the most impact on quality.
Measure (M)
  Determine how to measure the process and how it is performing.
  Identify the key internal processes that influence CTQs and measure the defects currently generated relative to those processes.

## Slide 88: Six Sigma: DMAIC
Analyze (A)
  Determine the most likely causes of defects.
  Understand why defects are generated by identifying the key variables that are most likely to create process variation.
Improve (I)
  Identify means to remove the causes of defects.
  Confirm the key variables and quantify their effects on the CTQs.
  Identify the maximum acceptance ranges of the key variables and a system for measuring deviations of the variables.
  Modify the process to stay within an acceptable range.
Control (C)
  Determine how to maintain the improvements.
  Put tools in place to ensure that the key variables remain within the maximum acceptance ranges under the modified process.

## Slide 89: ADDITIONAL HINT
Conduct a deep research on:
Business outsourcing
ABC system in stock Management (Graph)
Other related concepts
Thank u very much for your kind coperations!