## Slide 1: Drainage of Agricultural lands
Environmental impact of drainage
Methods; overview
Drainage requirement – soil types, climate, land use
Agricultural drainage planning, design and management
NIYONKURU Rose
Department of Irrigation and Drainage
UR-CAVM

## Slide 2
Water or hydrologic cycle
Notes: Local scale, major pathways of water movement
Solar radiation drives the water cycle.

## Slide 4: Land drainage
“Land drainage is removal of excess surface and
subsurface water from land to enhance crop growth,
including the removal of soluble salts from the soil”
International Commission on Irrigation and Drainage (ICID, 1979)

## Slide 5: Land drainage – Principles and methods
Why drainage?
Environmental impact of drainage
Methods; overview
  Surface drainage
  Subsurface drainage
  Controlled drainage
  Tube well Drainage systems
  Mole drainage
  Slit drainage

## Slide 6: Drainage Problem…?
About 25 million hectares of prime agricultural land became unproductive due to irrigation-induced water logging and salinity
30 – 50 per cent of the worlds’ irrigated lands developed some form of drainage problem
About 250 million hectares in rain fed cropland need improved drainage
Considerable increase in crop production could be achieved through drainage without additional land and water resources exploitation.
Notes: On a global scale, 170 million ha of cropland require drainage and/or flood protection. Drained lands are a very important part of our resource base on both global and national scales.

## Slide 7: Why drainage?

## Slide 8: Why land drainage?
Better access
to land
Improved
speed of work
and fuel use
Benefits to soil structure
and the environment
Reduced risks to
livestock health

## Slide 9: Why land drainage?
Better access to land;
Reduced duration/risk of waterlogging
Quicker accessibility of fields following any period of wet weather
Crop inputs more likely to be applied at optimum time
An extended growing and grazing season

## Slide 10: Why land drainage?
Improved speed of work and fuel use;
Better traction
Fewer cultivation passes
Reduced draught forces
Reduced wear and tear
Fewer wet areas to avoid

## Slide 11: Why land drainage?
Benefits to soil structure and the environment;
Less structural damage to soils
Reduced frequency and extent of livestock poaching
Better water infiltration
Reduced surface run-off and erosion

## Slide 12: Why land drainage?
Benefits to soil structure and the environment;
Reduced phosphorus and pesticide losses to water
Decreased potential for slug activity and reproduction, potentially reducing reliance on metaldehyde

## Slide 13: Why land drainage?
Reduced risks to livestock health;
Reduced survival of parasitic larvae
Snails carrying liver fluke do not thrive
Footrot and foul-of the-foot are less common
Udder hygiene for grazing stock is improved
Reduced risk of soil contamination during silaging operations

## Slide 14: Drainage to control ponding
Ponding is the accumulation of excess water on the soil surface

## Slide 15: Drainage to control water logging
Water logging is the accumulation of excess water in the root zone of the soil.

## Slide 16: Drainage to control water logging
Prolonged waterlogging under the surface may not be so obvious. Poor drainage conditions may be identified by:
Poor crop health or yields: overlaying a yield map onto a field drainage map can identify problem areas
High surface run-off rates and soil erosion
Limited field access without rutting or poaching (animal hoof damage) compared with other fields in the area

## Slide 17: Drainage to control water logging
Poor drainage conditions may be identified by:
The presence of wet-loving plant species, such as common rush and redshank
Susceptibility to drought due to poor root development and limited rainfall percolation into the soil

## Slide 18: Drainage to control water logging
If drainage problems are widespread across the field, it may be that:
Soil management is not adequate
No drains have been installed
Mole drains need to be renewed
In flatter fields, the outfall may simply be blocked
The drainage system requires maintenance or has reached the end of its useful life

## Slide 19: Environmental concern
Surface run-off may occur which can result in transport of ;
faecal material
sediment,
soil-borne diseases (eg clubroot)
nutrients or agrochemicals
to watercourses.

## Slide 20: Erosion

## Slide 21: Erosion – nutrient transport

## Slide 22: Drainage to control water logging
Combination of soils and climate create need

## Slide 23: Drainage to control salinization
Salinization is the accumulation of soluble salts at the soil surface, or at some point below the soil surface, to levels that have negative effects on plant growth and/or on soils.

## Slide 24: Markavvattning för att förebygga Försaltning

## Slide 25
Ritzema, 2008

## Slide 26: Fast and even drying
Even establishment
Good development, good root environment
Good bearing capacity

## Slide 27: Why drainage?
The aim of agricultural land drainage is to optimize agricultural production related to:
conservation of agricultural land
reclamation of agricultural land
optimization of crop yield
crop diversification
cropping intensification
optimization of farm operations

## Slide 28: Pore system in soil
Ratio of air and water in the pore system
Pore size distribution
Continuity and tortuosity
Storage and conductivity of water
Gas exchange
Storage and conductivity of heat
Possibility of root development

## Slide 29: Optimum composition for most crops

## Slide 30: Environmental impacts of drainage
Impact of drainage on soil conditions
  Physical effects
  Biological effects
  Chemical effects
Hydrological impact of a drainage system
Water quality impacts

## Slide 31
Installation of drainage system
Direct effects
Lower groundwater levels
Dryer soils
Indirect effects
Physical
Hydrological
Biological
Chemical
Environmental impacts of drainage

## Slide 32: Impact of drainage on soil conditions
Soil physical impacts
soil aeration
soil structure and consistency
soil temperature
irreversible shrinkage (gyttja soil)
subsidence (peat soils)

## Slide 33: Environmental impacts of drainage
Oosterbaan, 1994

## Slide 34: Soil Aeration
Process of Soil Aeration
Characterizing Soil Aeration
Factors Affecting Soil Aeration
Ecosystem Effects of Soil Aeration

## Slide 35
I. Process of Soil Aeration
O2 availability in field
  soil macroporosity (texture/structure)
  soil water content (proportion of porosity filled with air)
  O2 consumption by respiring organisms (plant roots and microbes)
Excess Moisture
  water saturated/waterlogged: condition when all or nearly all of the soil pores are filled with H2O
  adaption
Gas exchange
  mass flow
  diffusion

## Slide 36: Soil gas exchange

## Slide 37: Diffusion

## Slide 38: Demand - Storage
Demand: Productive crop, one cropping season (coarse estimation) |  | 
Water | 4 000 000 kg ha-1 | 4 000 m3 ha-1
Oxygen | 8 000 kg ha-1 | 10 000 m3 ha-1
Nitrogen | 200 kg ha-1 | 
Ca 20 % oxygen in air→ 50 000 m3 ha-1 |  | 
Assumption: Available water 200 mm → 2 000 m3 ha-1
Available air → 1 000 m3 ha-1
Crop demand: 2 storages of water
50 storages of air
Oxygen will last 2 to 3 days!

## Slide 39
II. Characterizing Soil Aeration
Composition
  O2
  CO2
  other gases
Air-filled porosity
  ideal composition
  O2 diffusion through water<<<<<air
Chemical redox potential
  redox
  role of O2
  other e- acceptors

## Slide 40: Composition of soil air (Volume%)
 | N2 | O2 | CO2 | CH4
Atmosphere | 78 | 21 | 0,035 | Trace
Soil air | 78 | 20 (0-20%) | 0,35 (0-5%) | Trace

## Slide 41: Composition of soil air CO2- concentration in soil
After Koorevaar et al., 1983

## Slide 42: CO2 content in soil

## Slide 43
II. Characterizing Soil Aeration
Composition
  O2
  CO2
  other gases
Air-filled porosity
  ideal composition
  O2 diffusion through water<<<<<air

## Slide 44: Ideal seed bed
Foto: Jens Blomqvist
Notes: Vad krävs för ett frö ska gro?
lämplig temperatur
tillräcklig syre och vattentillgång
friskt utsäde med bra energiinnehåll och frö som inte är skadade,
inga grobarhetshämmande substanser som försvårar groningen.
Därtill kommer ytterligare krav för grödans uppkomst.
Avståndet från frö till markytan får inte vara för långt eftersom energireserven hos fröet är begränsande
det får heller inte vara ett alltför kraftigt mekaniskt motstånd mot plantan vid tillväxt
får inte plantorna utsättas för skadedjur, sjukdomar eller fysisk samt kemisk påverkan (Håkansson, m.fl., 2010a)

## Slide 45: Soil aeration
Diffusion coefficient (m2 s-1) |  | 
Substance | O2 | CO2
Air | 2,3 • 10-1 | 1,8 • 10-1
Water | 2,6 • 10-5 | 2,0 • 10-5
Notes: Atmosfären: 78 % N2, 21 % O2, 0,035 % CO2
Markluft O2 ~20 % vid ytan till < 5 % längre ned i profilen
Låg O2 anaerobiskt (blöta jordar)
CO2 halter ofta 0,35 % ~ 10 ggr högre än i atmosfären
Transportprocesser
  Konvektivt flöde (massflöde); drivkraft en gradient i totalt gastryck.
  Diffusion; drivkraft en gradient i partialtryck (eller koncentration).

## Slide 46
III. Factors Affecting Soil Aeration
Drainage
Rates of respiration
Subsoil vs. topsoil
Soil heterogeneity
Seasonal differences
Effects of vegetation

## Slide 47
Factors Affecting Soil Aeration
Drainage
  Why are macropores important to soil aeration?
Rates of respiration
  2. What management activities can alter soil air composition?
Subsoil vs. topsoil
  3. Why do subsoils have lower O2 concentrations than surface soils?

## Slide 48
Factors Affecting Soil Aeration
D. Soil heterogeneity
  How do O2 and CO2 concentrations change within a profile?
  What effect does tillage have on aeration?
E. Seasonal differences
  6. Contrast spring vs. summer soil aeration.
F. Effects of vegetation
  7. What is an effect of one specific type of vegetation on soil aeration?

## Slide 49: Storage and heat conductivity
Substans | Heat capacity (MJ m-3 0C-1) | Heat conductivity (W m-1 0C-1)
Quartz | 2,0 | 8,8
Other minerals | 2,0 | 2,9
Organic material | 2,5 | 0,25
Water | 4,2 | 0,57
Ice | 1,9 | 2,2
Air | 0,0013 | 0,025
OM
Clay
Sand
Water content (vol%)
Notes: I det fall då vi har en helt uttorkad kvartssand kommer värmeöverföringen att ske 220 ggr så effektivt i partiklarna som mellan partiklar, separerade av luft. Om istället kontaktytorna mellan partiklarna är utfyllda med vatten
blir motsvarande siffra 16.
Effekten av vattenhalten på den termiska konduktiviteten är vanligtvis mindre betydelsefull i lerjordar eftersom de l) sällan torkar ut så starkt och 2) ej innehåller kvarts. Till skillnad från sandjorden finns i leran ingen, eller en mycket liten, direkt kontakt mellan mineralen. Alla mineral i ett aggregat kan dock betraktas som i det närmaste helt inneslutna i vatten. Vattnet blir därför så gott som alltid kontinuerligt medium i en lerjord. Vid stark upptorkning uppkommer sprickor mellan aggregaten men dessa sprickor får ibland en parallell orientering med värmeflödet. Dessutom kan kontakten mellan enskilda lerpartiklar förbättras i aggregaten eftersom de förs närmare varandra i samband med krympningen. Vi kan således förvänta oss betydligt mindre variationer i termisk konduktivitet för lerjordar och lägre maximala värden på grund av frånvaron av kvarts.
I en ren organogen jord kommer vattnet att få en högre termisk konduktivitet än det fasta materialet. Vattnet kan här i likhet med förhållandena i lerjorden betraktas som kontinuerligt medium, men eftersom inget annat material än vattnet självt kan förväntas att bidraga till markens förmåga att leda värme.

## Slide 50: Impact of drainage on soil conditions
Biological effects
plant establishment
root development
macroorganisms and microorganisms
mineralisation
nitrification
denitrification

## Slide 51: Wheat (winter) Emergence
Duration of water logging between
germination & emergence, (days)
Percent of seeds producing seedlings
4
8
20
0
0
100
80
A similar, dramatic
curve exists
for other crops

## Slide 52: Rooting depth

## Slide 53: Drainage distance – drainage effects
Tile
Drainage distance 96 m
Tile
Parcell harvest in a drainage trial with different drainage distance at Gunnarstorp 1949-1968, Skaraborgs län, crop winter wheat
Håkansson et al., 1974
Notes: 53

## Slide 54: Aerobic processes in arable soil
After McAfee, 1989

## Slide 55
Nitrogen flows
After Brady, 1984

## Slide 56: Impact of drainage on soil conditions
Chemical effects
reduction/oxidation state
pH
solubility of elements

## Slide 57: What is oxidation and reduction?
Oxidation and reduction are chemical reactions involving the exchange of electrons from one compound to another
Oxidation and reduction always happen together - when one compound loses an electron, another compound gains it
  Oxidation happens when electrons are lost
  Reduction happens when electrons are gained

## Slide 58: Oxidation and reduction in an aerobic setting
Organic matter in soil gives up 4 electrons (e-) which are received by O2. As a result, O2 is reduced.
Hydrogen ions (H+) react with the reduced O2 to form water (H2O).
  4 e- + O2 + 4 H+→ 2 H2O

## Slide 59: Oxidation and reduction in an anaerobic setting
Electrons (e-) from organic matter in soil are accepted by nitrate (NO3-) instead of O2.
Nitrogen (N) in NO3- is reduced; the N compound becomes nitrogen gas (N2)
Hydrogen ions (H+) react with oxygen from NO3- to produce H2O.
  10 e- + 2 NO3- + 12 H+→ 1 N2 + 6 H2O

## Slide 60: Summary slide
Organisms get energy for life through respiration
Respiration involves an exchange of electrons.
  One compound gains electrons (reduction)
  Another compound loses electrons (oxidation)
Carbon compounds consumed by organisms are oxidized and the electrons are gained by
  O2 in aerobic soil
  Chemical compounds like nitrate or sulfate in anaerobic soil

## Slide 61
Reaction sequence following submergence
Reaction sequence after draining
Chemical Reduction Sequence Following Submergence
O2
N2
Mn2+
Fe2+
NO3-
MnO2
Fe3+
CO2
CH4
SO4-2
H2S
H2O
Slightly Reduced
Moderately Reduced
Strongly Reduced
Oxidized
Notes: The boxes represent different chemical compounds in the soil. When the soil is aerated, the chemical compounds in the soil will be represented by the top set of boxes. The bottom set of boxes represent the chemical compounds in the soil after they are reduced. As you click on the slide (in presentation view), you can see the order in which the compounds are reduced and the change in form. The sequence of the compounds from left to right is the order in which they will be reduced starting with oxygen and ending with carbon dioxide.
When a soil is drained, oxygen begins to move into the soil and react with the reduced compounds. The reduced compounds are then oxidized in the reverse sequence starting on the right and moving to the left.

## Slide 62: Form of compounds in aerated versus submerged soil
Element | Aerated soil (Oxidized) | Submerged soil (Reduced)
Oxygen (O) | Oxygen gas (O2) | Water (H2O)
Nitrogen (N) | Nitrate ion (NO3-) | Nitrogen gas (N2)
Manganese (Mn) | Manganese IV ion (Mn4+) | Manganese II ion (Mn2+)
Iron (Fe) | Iron III ion (Fe3+) | Iron II ion (Fe2+)
Sulfur (S) | Sulfate ion (SO42-) | Hydrogen sulfide (H2S)
Carbon (C) | Carbon dioxide (CO2) | Methane (CH4)

## Slide 63: Chemistry and color
A change in chemistry results in a change of soil color
  bright colors indicate a well-drained soil
  submerged soils change to a gray or blue-green color (often referred to as gley)
Why is this?
  Reddish-yellowish brown colors are an indication of iron oxides in a well-drained environment
  Submergence causes iron to be reduced resulting in a different iron form and the gley color
Well-drained soil profile
Poorly drained soil profile

## Slide 64: Submergence affects soil pH
Soil pH is a measurement of hydrogen ions in the soil and it indicates whether soil is acidic or basic.
Submergence of soil typically causes a shift towards a more neutral soil pH. This is a result of the change in chemical compounds when soil is reduced

## Slide 65: Effect on soil pH when soils are submerged

## Slide 66: Availability of nutrients at different pH levels
The typical pH range for many submerged soils is 6.5-7. The 6 important crop nutrients in this chart are collectively more available at 6.5-7 compared to more acidic or basic pH values.

## Slide 67: Summary slide
In submerged soil, chemical compounds are reduced during respiration of anaerobic microorganisms
Compounds are reduced in order based on the amount of energy needed – nitrate is first because the least energy is required
This reduction process causes a shift in the chemical compounds found in submerged soil
This change in chemical compounds results in other changes such as soil color, soil pH, and availability of nutrients for plants

## Slide 68: Oxidation och reduktion under Aerobiska förhållanden
Organiskt material avger 4 elektroner (e-) vilka tas upp av O2 som reduceras.
Vätejoner (H+) reagerar med det reducerade O2 och bildar vatten (H2O).
  4 e- + O2 + 4 H+→ 2 H2O

## Slide 69: Oxidation och reduktion under Anaerobiska förhållanden
Elektroner (e-) från organiskt material tas upp av nitrat (NO3-) istället för av O2
Kvävet (N) i NO3- reduceras; Slutprodukten av N blir kvävgas (N2)
Vätejoner (H+) reagerar med syret från NO3- och bildar H2O
  10 e- + 2 NO3- + 12 H+→ N2 + 6 H2O

## Slide 70
Reaktionssekvens efter vattenmättnad
Reaktionssekvens efter dränering
Kemisk reduktionssekvens som följer efter vattenmättad av jord
O2
N2
Mn2+
Fe2+
NO3-
MnO2
Fe3+
CO2
CH4
SO4-2
H2S
H2O
Något Reducerande
Måttligt Reduktion
Starkt Reducedande
Oxidation
Notes: The boxes represent different chemical compounds in the soil. When the soil is aerated, the chemical compounds in the soil will be represented by the top set of boxes. The bottom set of boxes represent the chemical compounds in the soil after they are reduced. As you click on the slide (in presentation view), you can see the order in which the compounds are reduced and the change in form. The sequence of the compounds from left to right is the order in which they will be reduced starting with oxygen and ending with carbon dioxide.
When a soil is drained, oxygen begins to move into the soil and react with the reduced compounds. The reduced compounds are then oxidized in the reverse sequence starting on the right and moving to the left.

## Slide 71: Aeroba versus anaeroba förhållanden
Ämne | Aerob mark (Oxiderad) | Anaerob mark (Reducerad)
Syre (O) | Syrgas (O2) | Vatten (H2O)
Kväve (N) | Nitrat-jon (NO3-) | Kvävgas (N2)
Mangan (Mn) | Mangan IV jon (Mn4+) | Mangan II jon (Mn2+)
Järn (Fe) | Järn III jon (Fe3+) | Järn II jon (Fe2+)
Svavel (S) | Sulfat-jon (SO42-) | Vätsulfid (H2S)
Kol (C) | Koldioxid (CO2) | Metan (CH4)

## Slide 72: Effekter på pH i marken när sura, neutral, och basiska jordar är anaeroba
Jord med högt pH
Jord med lågt pH
Jord med neutralt pH
Basisk
Sur
Antal veckor efter översvämning

## Slide 73: Växttillgänglighet av ämne vid olika pH

## Slide 74: Hydrological impact of a drainage system
partition of runoff
runoff event; lag time, peak outflow rate, base flow and total outflow

## Slide 75: Hydrological impact
Outflow volume
  Land development involving drainage and conversion to agriculture INCREASES total annual outflows by about 10-20 percent

## Slide 76
Outflow volume
  Controlled drainage may REDUCE outflows to pre-development amounts, (Depends on management intensity)

## Slide 77: Hydrological impact
Peak Outflow Rates
  Land development involving drainage and conversion to agriculture Dramatically INCREASES Peak Outflow Rates

## Slide 78: Impact on water quality
Nutrient (N&P) Concentration
  Land development involving drainage and conversion to agriculture INCREASES nutrient (nitrogen and phosphorus) concentrations in outflow

## Slide 79: Impact on water quality

## Slide 80: Nutrient content in outflow
Surface runoff
Subsurface runoff
Particular Phosphorus (PP)
Sediments
Dissolved Nitrogen (DN)
DRÄNERINGSCENTRALEN RF
Dissolved Phosphorus (DP)
Particular Nitrogen (PN)

## Slide 81
Excess water
Large pores filled
Diffusion declines
Continued decomposition and biotic activity consume available soil oxygen
Soil oxygen content decline
Carbon dioxide content builds up
Low redox potentials
Accumulation of
Reduced Fe and Mn
HxS at toxic levels
Root damage, restricted growth
Reduced uptake of nutrients
Reduction in plant growth and yield
Denitrification
Increased leakage
After Ravelo, 1978 and Patwardhan et al, 1988
Notes: Processer i marken orsakade av ett överskott av vatten som leder till hämmad tillväxt och skörd

## Slide 82: Drainage system
A field drainage system, which prevents ponding water on the field and/or controls the water table.
A main drainage system, which conveys the water away from the farm.
An outlet, which is the point where the drainage water is led out of the area.

## Slide 83
Field drainage system (internal)
surface drainage system (by gravity)
conventional system
controlled system
subsurface drainage system (by gravity or pumped)
conventional system
Reglerbara system
graded land
bedded land
bunded basins
bunded terraces
subsurface, open ditches
sub soiling
Reglerbar dränering
Vertikal dränering
Main drainage system (external)
deep collectors (pipes, ditches)
disposal drains
shallow collectors (channels, ditches)
deep main drains
Outlet
Dräneringssystem
Oosterbaan, 1994

## Slide 84: Drainage systems
Oosterbaan, 1994

## Slide 85: Drainage system

## Slide 86: Field drainage systems
Surface drainage
  Graded land
  Bedded land
Subsurface drainage
  Pipes, tiles
  Tubewell drainage
  Mole channels
  Slit drainage
  Controlled drainage
Notes: Methods of land drainage used on agricultural land are surface drainage, subsurface drainage, dikes with pumped drainage outlets and tubewell drainage. A surface drainage system removes excess water from the soil surface and the upper root zone in order to prevent water ponding on the soil surface.

## Slide 87
Illustration; Lena Granell

## Slide 88
Foto: Stig Svenmar

## Slide 89: Dikes
Illustration; Lena Granell

## Slide 90: Surface drainage
Surface drainage is the removal of excess water from the surface of the land by diverting it into improved natural or constructed drains, supplemented, when necessary, by the shaping and grading of the land surface towards such drains.

## Slide 91: Surface drainage
A surface drainage system always has two components:
Open field drains to collect the ponding water and divert it to the collector drain.
Land forming to enhance the flow of water towards the field drains.

## Slide 92: Surface drainage

## Slide 93: Surface drainage

## Slide 94: Surface drainage

## Slide 95: Surface drainage, types of drainage flows

## Slide 96: Surface drainage

## Slide 97: Land forming
Land forming means changing the surface of the land to meet the requirements of surface drainage or irrigation. There are three land-forming systems:
bedding
land grading
land planing

## Slide 98: Land forming, bedding
Bedding is a surface drainage method achieved by ploughing land to form a series of low beds, separated by parallel field drains.

## Slide 99: Land forming, land grading
Land grading is forming the surface of the land to predetermined grades, so that each row or surface slopes to a field drain.

## Slide 100: Land forming, land planing
Land planing is smoothing the land surface with a land plane to eliminate minor depressions and irregularities without changing the general topography.

## Slide 101
Foto: Anuschka Heeb
Open ditch

## Slide 102
Foto: Anuschka Heeb
Half covered ditch

## Slide 103
Foto: Anuschka Heeb
Pipe drained

## Slide 104: Subsurface drainage
Subsurface drainage is the removal of excess water and dissolved salts from soils via groundwater flow to the drains, so that the water table and root-zone salinity are controlled.

## Slide 105: Subsurface drainage

## Slide 106: Subsurface drainage system
drainage outlet
main drainage channel
some collector drains
field or lateral drains
Notes: The main drainage channel collects runoff from one or more collector drains. It discharges its water via a pumping station or by gravity into a river, a lake, or the sea at a suitable outlet. The main drainage channel is often a canal stream, which runs through the lowest parts of the agricultural area. Both collectors and lateral drains can be open ditches or pipe drains.

## Slide 107: Subsurface drainage

## Slide 108: Surface/subsurface drainage
can receive overland flow
functional at soil frost
evacuate the standing water from the rice fields
occasional high-intensity rainfall (say more than 50 mm/day)
loss of land
interference with the irrigation system
the splitting up of the land into small farm blocks, which hampers farming operations,
they are a maintenance burden.

## Slide 109
Surface and Subsurface Drainage Hydrographs
Drainage Outflow, cm / day
10
20
30
40
50
60
70
80
90
0
0.5
1.0
1.5
2.0
2.5
3.0
Time, hrs
0
0.1
0.2
0.3
0.4
Rain, cm / hr
Surface Drainage
Subsurface Drainage
Total Rainfall = 32.5 mm
Total Outflow for
Surface Drainage = 2.54 cm
Total Outflow for Subsurface Drainage = 2.74 cm
Total Outflow for
Surface Drainage = 25.4 mm
Total Outflow for Subsurface Drainage = 27.4 mm
Subsurface Drainage

## Slide 110: Controlled drainage

## Slide 111
Controlled Drainage

## Slide 112: Function and management
when to raise and lower the control structure
what height to maintain the weir in the control structure

## Slide 113: Function and management

## Slide 114: Environmental Benefits
Improve drainage water quality
Controlled drainage has been recognized as a best management practice (BMP)
Reduce nitrates leaving the site by up to 50% compared to conventional drainage
Improves the off-site water quality in terms of herbicides, pesticides, sediments and other nutrients

## Slide 115: Economics
higher initial cost than a conventional drainage system.
potential for higher yields,
less varied yield results
lower operational cost
require more attention to properly manage the water table level

## Slide 116
Agricultural drainage systems can be beneficial both from an agricultural and an environmental point of view

## Slide 117: Tube well Drainage systems
Controlling the watertable and salinity by pumping from a series of wells
Water is discharged into open ditches

## Slide 118: Tube well Drainage systems
Boehmer and Boonstra, 1994

## Slide 119: Vertical drainage systems
Areas with Artesic water

## Slide 120: Tube well Drainage systems
Less total length
Excessive earth moving is avoided
Less to maintain
Watertable may be lower to much greater depth
Reduce artesian pressure
Water may be used for irrigation
More costly to maintain and operate
Energy requirement
Legal regulations
Not economically feasible in small areas
Salt content of drainage water can be higher

## Slide 121: Mole Drainage systems
Heavy soils of low hydraulic conductivity (< 0.01 m/day)
Unlined circular soil channels
Low costs
Restricted functional time

## Slide 122: Mole drainage

## Slide 123: Mole drainage
http://www.tgdrains.com.au/

## Slide 124: Mole drainage

## Slide 125: Mole drainage

## Slide 126: Mole Drainage systems
Clay content > 45%
Structured stability on wetting
Timing on moling operation (best during dry period)
Moling depth (commonly 0.4 - 0.7 m)
Moling drain spacing (closer that required 2 to 3.5 m)
Length of mole run (commonly 20 to 100 m)

## Slide 127: Slit drainage
Surface drainage can be improve by slit drainage
A series of 5-7 cm wide and 40–60 cm deep, cut directly in the surface and filled with a course, free-draining material. Normal cc-distances are from 0,5 m and forward depending on need.
Important is that these slits have a direct connection to an underground pipe network. The slits lay out are usually right across the pipes.

## Slide 128: Slit drainage
S
Slits 5-7 cm wide
50 cm > apart
40-60 cm deep
After http://www.lancoturf.com/cadre-slit.htm

## Slide 129: Slit drainage

## Slide 130: Slit drainage

## Slide 131: Controlled drainage
bild: Jord- och skogsbruksministeriet 2000

## Slide 132: Management of drainage water
Improve water quality
Reduce outflow
Reuse of drainage water

## Slide 133: Characteristics of drainage water quality
Salts and major ions
Toxic trace elements
Agropollutants
Sediments

## Slide 134: Water quality concerns for water uses
Crop production
Living aquatic resources, fisheries and aquaculture
Livestock production
Concerns for human health

## Slide 135: Management of drainage water
Improve water quality
Cropping patterns
Use of agricultural inputs
Drainage techniques and design

## Slide 136: Management of drainage water
Reduce outflow
Irrigation and drainage management
Drainage techniques and design

## Slide 137: Management of drainage water
Reuse of drainage water
Reuse in conventional crop production
Crop substitution and reuse for irrigation of salt tolerant crops
Reuse in Integrated Farm Drainage Management systems (IFDM systems)

## Slide 138: Management of drainage water Reuse of drainage water for crop production
FAO Irrigation and Drainage paper 61, 2002

## Slide 139: Management of drainage water irrigation of salt tolerant crops
FAO Irrigation and Drainage paper 61, 2002

## Slide 140: Management of drainage water Reuse in IFDM systems
FAO Irrigation and Drainage paper 61, 2002

## Slide 141: Management of drainage water Reuse in IFDM systems
FAO Irrigation and Drainage paper 61, 2002